## Slide 1: Roboticorp: Implementation Planning
Morgan, Laura
Miaw, Jireh
Hauser, Steven
Dworak, Catherine
Bertoglio, David

## Slide 2: Specification Techniques
Defined command structure
Defined command types
Divided specification into command type
Defined each command possibility for the command types

## Slide 3: Details
10 character messages
Base Station to Robot Commands:
  No-Op
  Move Straight (MS)
    Byte 2 is forward or backwards (F/B)
    Bytes 3-9 is distance (#), can be null (0s)
  Move Arc (MA)
    Byte 2 is forward or backwards (F/B)
    Byte 3 is left or right (L/R)
    Byte 4-6 is radius (# degrees)
    Byte 7-9 is distance (#), can be null (0s)
  Turn (TN)
    Byte 2 is left or right (L/R)
    Byte 3-9 is radius (# degrees), can be null (0s)
  Stop (ST)
  Read Sensor (RS)
    Byte 2 is sensor type (U for Ultrasonic, T for touch, M for sound, L for light)
    Bytes 3-9 are 0
  Set Speed (SS)
    Byte 2 is Motor/Motor combination
    Bytes 3-9 is the new speed
  Read All Sensors (RA)

## Slide 4: Details Cont.
Robot to Base Station Commands:
  Acknowledgment (AK)
  Sensor Error Message (ERS)
  Motor Error Message (ERM)
  Sensor Data Message (SD)
    Byte 2 sensor type (U for Ultrasonic, T for Touch, M for Sound, or L for Light)
    Bytes 3-9 sensor data
Message Number | Description
0000001 | Error with sensor in port 1
0000002 | Error with sensor in port 2
0000003 | Error with sensor in port 3
0000004 | Error with sensor in port 4
Message Number | Description
0000001 | Error with motor in port A
0000002 | Error with motor in port B
0000003 | Error with motor in port C

## Slide 5: Details Cont.
Message Sending:
  Message is sent from base station to robot
  Robot receives message and checks for error
  If error, the robot waits for time out
  If correct, the robot sends an ACK to the base station
  On timeout, base station will resend the message

## Slide 6: Functionality
The Testing Tool
  Uses command line instructions to implement the protocol and send a message to the robot
  Supports all the commands described in the protocol that the base station needs to send to the robot

## Slide 7: Design
The testing tool was designed using sample code available on collab to create the USB/Bluetooth connection between computer and robot
Then the communications protocol was implemented using user entered input to create messages that are sent to the robot.
The Main goal was to create messages using protocol to send to the robot

## Slide 8: Implementation Status
Our development support tool has a basic implementation
Some user commands are set to default values (Moving in an arc and a help listing method).
Otherwise messages are created correctly, error handling is to be completed once we decide on a method for error checking